1. Bandpass Cavity Filter 66 MHz – 88 MHz

| SPECIFICATIONS | BP-6688-1 |
| --- | --- |
| Frequency Range (MHz) | 66-88 |
| Bandwidth at 3 db | 1.5 MHz |
| Insertion Loss - db | 2.0 |
| Rejection @ 40 db | 10 MHz |
| Impedance in Ω | 50 |
| VSWR | 1.5: 1 |
| Dimensions L X W X H – mm | 120 X 105 X 32 |
| Connector Type | BNC, N type, SMA |

2.  Bandpass Cavity Filter 140 MHz – 175 MHz

| SPECIFICATIONS | BP-1418-1 | BP-1418-2 |
| --- | --- | --- |
| Frequency Range (MHz) | 140 - 175 |
| Bandwidth at 3 db | 2.0 MHz | 4.0 MHz |
| Insertion Loss - db | 2.25 | 1.5 |
| Rejection @ 40 db @ 45 db | 16 MHz - | - 20 MHz |
| Impedance in Ω | 50 |
| VSWR | 1.5: 1 |
| Dimensions L X W X H – mm | 120 X 105 X 32 |
| Connector Type | BNC, N type, SMA |

3. Bandpass Cavity Filter 405 MHz – 480 MHz

| SPECIFICATIONS | BP-1418-1 | BP-1418-2 |
| --- | --- | --- |
| Frequency Range (MHz) | 405 - 474 |
| Bandwidth at 3 db | 3.0 MHz | 6.0 MHz |
| Insertion Loss - db | 1.5 | 1.0 |
| Rejection @ 40 db @ 45 db | 30 MHz - | - 40 MHz |
| Impedance in Ω | 50 |
| VSWR | 1.5: 1 |
| Dimensions L X W X H – mm | 180 X 105 X 32 |
| Connector Type | BNC, N type, SMA |