A. Frequency Range : 70 MHz to 86 MHz

| SPECIFICATIONS | PS-1315 |
| --- | --- |
| Frequency Range (MHz) | 70 MHz – 86 MHz |
| Bandwidth at 3 db - MHz | 2.0 min |
| Insertion Loss - max | 2.0 db @ Fc |
| Rejection - db min | 40 db @ Fc +/- 29 MHz |
| Impedance (Ω) | 50 |
| Return Loss – db min | 14 |
| Dimensions L X W X H mm | 150 X 102 X 32 |
| Connector Type | BNC, N type |

B. Frequency Range : 130 MHz to 170 MHz

| SPECIFICATIONS | PS-1315 | PS-1317 |
| --- | --- | --- |
| Frequency Range (MHz) | 130 - 154 | 150 - 170 |
| Bandwidth at 3 db - MHz | 2.0 min |
| Insertion Loss - max | 2.25 db @ Fc |
| Rejection - db min | 45 db @ Fc +/- 6 MHz |
| Impedance (Ω) | 50 |
| Return Loss – db min | 14 |
| Dimensions L X W X H mm | 125 X 102 X 32 | 150 X 102 X 32 |
| Connector Type | BNC, N type |

C. Frequency Range : 465 MHz to 505 MHz

| SPECIFICATIONS | PS-1315 |
| --- | --- |
| Frequency Range (MHz) | 465 - 505 |
| Bandwidth at 3 db - MHz | 4.0 min |
| Insertion Loss - max | 2.0 db @ Fc |
| Rejection - db min | 50 db @ Fc +/- 29 MHz |
| Impedance (Ω) | 50 |
| Return Loss – db min | 14 |
| Dimensions L X W X H mm | 80 X 102 X 32 |
| Connector Type | BNC, N type |