SSB Crystal Filters:

Custom SSB Type Crystal Filters are available from 1.4 MHz to 21.4 MHz. Monolithic and discrete designs are used in our SSB products. SSB crystal filters are used extensively in frequency division multiplex, military HF transceivers and marine telephones. The specifications presented here have been achieved in production environment. New filters are designed by engineering and manufactured on regular basis. Therefore, if the desired frequency and specifications (electrical and/or mechanical) are not listed below, please contact the factory or the nearest office to discuss your special requirements.

| OPT Model | Carrier Freq. | Carrier Reject | PASSBAND | Loss max | Ripple max | STOPBAND | Impedance Ω / / PF | Temper. RANGE | Package Dimen. LXWXH |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | MHZ | db | db | KHz | db | db | db | KHz | Zin | Zout | C | mm |
| XF-9724 | 1.400 | 15 | 6 | - 350 - 2700 | 6 | 2.0 | 60 | + 500 + 3400 | 50 | 50 | -35/ +70 | 76.2X27X30.5 |
| XF-9725 | 1.400 | 15 | 6 | + 350 + 2700 | 6 | 3.0 | 25 60 | - 500 -3400 | 50 | 50 | -35/ +70 | 76.2X27X30.5 |
| XF-9733 | 1.400 |  | 2 | +/- 100 | 4 | 2.0 | 60 | +/- 300 +/- 1200 | 50 | 50 | -35/ +70 | 76.2X27X30.5 |
| XF-9588 | 1.650 | 15 | 6 | - 350 -2500 | 3 | 1.5 | 60 | + 1500 - 4000 | 50 | 50 | -35/ +70 | 65.6X44.5X33.3 |
| XF-9589 | 1.650 | 15 | 6 | + 350 + 2500 | 3 | 1.5 | 60 | + 2100 - 5000 | 50 | 50 | -35/ +70 | 65.6X44.5X33.3 |
| XF-3919 | 1.750 | 25 | 2 | + 300 + 3400 | 6 | 1.5 | 35 | - 300 + 4500 | 250 | 190 | -40/ +75 | 95.2X50.8X25.4 |
| XF9829* | 4.800 | 20 | 6 | - 300 - 3100 | 3.5 | 2.0 | 60 | + 400 - 3900 | 200 | 200 | -40/ +85 | 36.1X27.2X19.0 |
| XF-9590 | 5.000 | 10 | 6 | + 250 + 2800 | 6 | 2.0 | 50 | - 1500 + 4500 | 50 | 50 | -35/ +75 | 57.2X25.4X19.1 |
| XF-9591 | 5.200 | 10 | 1.5 | + 300 + 3400 | 5 | 0.5 | 60 | - 1000 + 4570 | 1500 | 1500 | -20/ +75 | 57.2X25.4X19.1 |
| XF9745* | 5.250 | 15 | 2.5 | + 350 + 3400 | 4.5 | 1.0 | 60 | - 1000 + 5000 | 250 | 250 | -40/ +85 | FK-21 |
| XF-9746 | 5.251 |  | 3.0 | +/- 120 | 4.5 | 0.5 | 60 | +/- 2000 | 250 | 250 | -40 +85 | 25.6X19.3X24.2 |
| XF-9592 | 6.120 | 15 | 2.0 | + 300 + 3850 | 1.5 | 0.5 | 60 40 | - 400 + 6000 | 1000 | 1000 | -20 +70 | 65.1X30.2X23.0 |
| XF9789* | 8.400 | 10 | 2.5 | + 350 + 3400 | 4.5 | 1.5 | 60 | - 1000 + 5000 | 50 | 50 | -40/ +85 | 40X20X14 |
| XF-9593 | 10.500 | 10 | 2.0 | + 350 + 3000 | 5.0 | 2.0 | 60 60 | - 1500 + 5000 | 250 | 250 | -30/ +60 | 58.8X19.1X19.1 |
| XF-9594 | 10.500 | 10 | 2.0 | - 300 - 3000 | 4.0 | 1.0 | 60 60 | + 1500 - 5000 | 250 | 250 | -30/ +60 | 58.8X19.1X19.1 |
| XF-8739 | 10.700 | 15 | 3.0 | - 400 - 2700 | 6.0 | 2.0 | 60 60 | + 650 - 3400 | 600 | 600 | -30/ +60 | 50X40X20 |
| XF-8739 | 10.700 | 15 | 3.0 | - 400 - 2700 | 6.0 | 2.0 | 60 60 | + 650 - 3400 | 600 | 600 | -30/ +60 | 50X40X20 |
| XF-9740 | 10.700 | 15 | 3.0 | + 400 + 2700 | 6.0 | 2.0 | 60 60 | - 650 + 3400 | 600 | 600 | -30/ +60 | 50X40X20 |
| XF-9812 | 21.400 | 10 | 6.0 | - 400 - 2600 | 4.0 | 2.0 | 40 | + 700 - 4000 | 1800 | 1800 | -20/ +70 | FK-10 |

*SPECIAL CHARACTERISTICS:

- XF-9829 - Group Delay of  800 μsec @ Fo and Inband IM of   50 db min @ -10 db level                     Outband IM of  60 db min @ -10 dbm level

- XF-9745 - Group Delay of  +/-300 μsec from 5.250600 MHz to 5.252750 MHz and Inband IM of  60 db min @ -30 dbm level

- XF-9789 - Group Delay of  +/-250 μsec from 8.400600 MHz to 8.402750 MHz and Inband IM of  52 db min @ -30 dbm  level